Synchronizing IIAB Modules Between Central Server (father) and RPI Hotspots
This document describes the approach to synchronize IIAB modules, such as en-test-eldp, between the central server (M73-1, we call it “father”) and multiple Raspberry Pis deployed across the Minawao camp.
------
Current Setup
- M73 Server (“father”): Central IIAB server hosting master content.
- Raspberry Pis: Distributed IIAB nodes in the field (kiosk, hospital, market).
- Access:
  - SSH for command-line management.
  - FileZilla (SFTP) for file transfers.

LAN-Based SFTP (FileZilla)
1. Connect Father and Pis to LAN.
2. On a laptop, open FileZilla: connect to Father and each Pi via SFTP, each pi on a new tab (using FileZilla, site manager).
3. Navigate to module path in Father,
4. Drag and drop module files from Father to each Pi, in the respective path.
5. Refresh IIAB on each Pi.
Pros: Fast, reliable, no monitor needed.
Cons: Pis must be physically in our office every time we want to update the content. Manual update is not problem-free and drag-and-drop or file-selection errors are possible.
-----
Conclusion
This design ensures that the latest IIAB module can be copied to all the Pis relatively efficiently, when connected on the same LAN. We will implement this design for our upcoming milestone 1—three Pis accessible at three strategic location on Thursday Oct 16, next market day. However, development of a more efficient solution remains necessary, especially for when there will be more Pis available.